Hello Everyone,

This is for anyone who is running Win98, and can't resolve

host names (like, www.penny-arcade.com) to an IP address -

you can't surf the web, but can ping stuff (Layer 3

connectivity is good, but the TCP stack is messed up on

yer PC). Here were my sypmtoms and resolution:

What started the whole problem

1. I had to remove my NIC to troubleshoot another PC, so I

removed all objects within the Network Configuration tab.

2. I put the NIC back into my PC, added the drivers, and

configured the TCP/IP settings.

Symptoms

1. Could not surf the net

2. Could not resolve any websites to an IP address, except

for www.yahoo.com (but I still surf yahoo by IW - really

weird).

3. I could not run a web server or FTP server - the FTP

server would give me "could not open socket, 10047 winsock

error". It was almost as if TCP/IP was not installed on my

PC, yet I could ping crap on my LAN, and on the internet.

4. I knew that it wasn't a NIC hardware or IP config

issue, since I have the same damn config on my Win2k dual-

boot (same machine), and everything worked fine.

Resolution

1. Wasted 9 hours of my life researching this on the

Internet, and found this awesome fix, to basically remove

the TCP/IP stack (winsock), and restore it to default

settings.

2. The fix is found below. I will also attach it as a text

file, for your convenience:

Hi! I work for an ISP in tech support, and have come

across the

"Newdot~2.dll is missing" error messages from NEW.net

software a few times,

and your website saved the day.  BTW, there's a fix I

have to use sometimes,

called the "Winsock2 Fix" which does NOT require a

reinstall of windows but

has the effect of replacing the winsock reg keys.  I user

it in situations

where nothing else has helped for browsing issues, and

especially when some

3rd party software has modified winsocks and TCP/IP in

general.  You may

have already tried this, if so, let me know.  I'm sorry

if some of it is

redundant or you know it already, but I'll just give the

full spiel in case

you haven't.

Here are the steps I use:

<<<< THIS ONLY WORKS FOR win98 FE, SE, and winME >>>>

1. EXTREMELY IMPORTANT - make sure that the person has

the *.cab files for

their version of windows, NOTE WHERE THEY ARE (what

DIR).  Usually it's

C:\windows\options\cabs, sometimes for winME it's

C:\windows\options\install, BUT NOT ALWAYS. Before I'll

TOUCH the network

stack or winsock.dll & wsock32.dll, I ALWAYS verify this

by searching for

win.com and then w*.cab to compare the dates. For

example, win.com with a

date of 4-23-99 indicates win98 SE, so as long as the cab

files

(win98 21.cab to win98 74.cab) have the same date, it's

all good.

win.com 05-11-98        win98 FE

win98 21.cab to win98 69.cab

win.com 04-23-99        win98 SE

win98 21.cab to win98 74.cab

win.com 06-08-00        winME

win 08.cab to win 22.cab

2. Go into Control Panel > Network, and note which

components are installed.

Make sure to hit cancel out of network stack, otherwise

often windows will

want to restart, even if you haven't made any changes.

3. Go into Control Panel > Add/Remove Programs > Windows

Setup Tab, click on

"Communications" to highlight, then click on Details.

Note which items are

checked

4. Uncheck ALL items in Communications, either

individually or by getting

out of "Details" and un-checking the check next to

Communications as a

whole.  Hit Apply, say NO to prompt for restarting. Hit

OK and close out of

Add Remove Programs

5. Go into Control Panel > Network again.  You may notice

that some or all

components are missing. LEAVE any hardware adapters that

are present, like

NIC cards, IR ports, TV/Data Adapters, NDIS 1394 cards,

unless you feel like

re-installing the drivers for them (I never do because we

can't re-install

drivers for people). Otherwise remove all components and

ALL SOFTWARE

adapters like Dial Up Adapter(DUA), MS Virtual Private

Networking (VPN)

Adapter, Internet Connection Sharing (ICS), ALL CLIENTS

like Client for

Microsoft Networks (CFMSN) or Microsoft Family Logon, and

ALL PROTOCOLS,

such as TCP/IP, netBEUI, IPX/SPX. Once this is done, hit

OK. I usually have

the user restart at this point, but you don't HAVE to.

6. Once restarted go into the Registry, back it up first,

and do something

with these keys (either rename or delete).  I usually

have people delete

them, but I like your idea of renaming.

HKey Local Machine\System\CurrentControlSet\Services\Remote

Access

HKey Local Machine\System\CurrentControlSet\Services\Winsoc

k

HKey Local Machine\System\CurrentControlSet\Services\Winsoc

k2

HKey Local Machine\System\CurrentControlSet\Services\VxD\Wi

nsock

HKey Local Machine\System\CurrentControlSet\Services\VxD\Wi

nsock2

7. Once this is done you HAVE to restart.

8. Go back into Control Panel > Add/Remove Programs >

Windows Setup Tab,

click on Communications and hit Details.  Either re-check

those entries

which were checked before, or at least check Dial Up

Networking (DUN) and

Hyperterminal.  Hit Apply, say NO if prompted to restart.

Hit OK out of

Add/Remove Programs

9. Go back into Control Panel > Network.  Add back any

components that were

present before, or at least make sure that CFSMN, DUA and

TCP/IP are

installed.  Sometimes IPX/SPX > DUA, netBEUI > DUA will

interfere with

browsing, so if it was there before I leave it out this

time. When done hit

OK and let windows install the components again

10. Restart (usually prompted to after step 9).  What we

have done is taken

out just about all the windows communications and

networking components,

made it so that windows can't find the reg keys and HAS

to install new ones,

and then have windows reinstall original files and

components (original to

the OS version, unmodified by 3rd party software).

<<<<<<<<<<<<<<<<<<<<<<<<<<<<<        NOTES:

>>>>>>>>>>>>>>>>>>>>>>>>>>>>>

--- In worst-case scenarios, you have to rename some

*.386 files,

pppmac.vxp, and a few others to FORCE windows to install

new copies.

--- If windows has not installed anything from the CAB

files before, it will

ask for the win98 or winME disk, with the only choice

as "OK".  If the files

ARE on the disk, there you go, if not, hit OK anyway, and

you'll get a

message that such-n-such file cannot be found.  Then at

the bottom of this

window you can instruct windows to look in the DIR where

the cab files are,

such as C:\windows\options\cabs.

--- VERSION CONFLICTS:  If any version conflicts come up,

if the file is

"Secure32.dll" I hit "YES" to keep the existing version,

OTHERWISE, hit "NO"

to overwrite existing versions, thereby letting windows

replace possible

corrupt components with fresh ones.

--- This fix does NOT touch winsock.dll, wsock32.dll, or

rasapi32.dll, so if

these files are corrupt, i.e. their file date does not

match that of

win.com, they have to be extracted separately through SFC.

--- At work I have to disclaimer people about the fact

that doing this fix

can interfere with their network setup, because it

completely rips it out

and re-builds it.  So I usually only do this fix on stand-

alone machines

with dial up access.

This fix may look a little drawn out at first, but really

I just gave the

long-winded version.  Basically its uninstalling

communications, ripping the

network stack, either renaming or deleting the reg keys,

and reinstalling

the comms and the network again, with a bunch of

disclaimers.  With a person

that knows their way around the computer and is willing

to work with you, it

takes about 15-20 minutes.  For absolute beginners it can

take 45 min to

1hr, but this is over the phone directing the USER to do

all this.  Either

way I find that it does fix a browsing issue in the

majority of cases, and

is better than having someone back up everything,

reformat, reinstall the

OS, and reinstall all programs and files again, IF that

can be avoided.

Anyway, enough rambling, please let me know if this

helps, if you've tried /

know of this fix, or if this STILL wouldn't get you out

of uninstalling and

reinstalling the Os